Scène
Modèle
Motion Model
 From the base class
Motion Model , motion model classes specific to a particular dimensionality of
movement OneD Motion Model , TwoD Motion Model are ThreeD Motion Model
 are derived (again defined in the file SceneLib/Scene/models base.h ).

Feature Measurement Model
 The base class Feature Measurement Model is parent to two special types of
second tier base classes, Partially Initialised Feature Measurement Model
 and Fully Initialised Feature Measurement Model which describe the behaviour
of feature measurements during and after initialisation.

 This splitting into two different classes is to represent the fact that different
types of probability propagation are often required during and after feature initialisation
in SLAM. The specific example which led to this design was the use of
point features in high frame-rate monocular visual SLAM. Here, the approach
which has proven to work well is to represent a just-initialised point feature
with a line parameterisation which lives in the main EKF SLAM map plus an
independent particle distribution along the depth dimension. The reason for
this is that the dominant uncertainty in a just-initialised point, along the depth
dimension, is not well-represented with a Gaussian distribution. The assignment
of an independent particle distribution for this coordinate of the point is
of course an approximation, but works well because over several measurements
it rapidly collapses. Once the particle distribution has collapsed into something
11
which looks Gaussian, the line representation plus particle distribution is converted
into a standard point representation in the main SLAM map (see [? ] for
more on this technique for monocular feature initialisation).